Heritage Conservation Briefs

## Energy & Waste Conservation

Heritage buildings store embodied energy Rehabilitating heritage buildings conserves more energy than constructing a new building Heritage conservation reduces construction and demolition wastes

# When a heritage buildings is demolished, the stored embodied energy goes to waste

The energy used in the lifecycle of a building, called the embodied energy, includes all the non-renewable energy consumed to:

1) Acquire, process, manufacture,

and transport building materials, and

construct the building (initial energy),

2) Maintain and repair the building

(recurring energy),

3) Operate the building (operating energy),

and

4) Demolish and dispose of the building.

A Canadian study examined the total life-cycle energy-use in a 4620 m2 (50,000 ft2) three-storey, generic office buildings.

The graph shows that, on average, the total

embodied energy of such a building

increases by 56.5% by the time it is 25,

144% by the time it is 50, and 325% by

the time it is 100 years old.  When the

building is demolished, this embodied

energy will be wasted.

(Building and Environment, 1996)

Maintaining the structure conserves a large

portion of a building’s embodied energy

The above Canadian study found that a 50% of

a building’s initial embodied energy is due to

the structure and envelope (see pie chart).

When a building is rehabilitated, the embodied

energy of these components is conserved.

(Building and Environment, 1996)

The rehabilitation of heritage buildings conserves embodied energy

A study of the Angus Technopole Building, a Montreal factory built in the early 20th century, compared rehabilitation and adaptive reuse of the building into a residential complex to demolition and construction of a new building on the same site.  It illustrated that rehabilitation required 5,169 Gigajoules (Gj) of energy, while demolition and new construction required 13,734Gj of energy.  The restoration used 8,565Gj less energy than demolition and building anew.

(The Athena Institute, 2004)

# Heritage conservation reduces the waste stream to landfills

In 2000, 12% of Canada’s waste disposal was from construction and demolition sources. (Statistics Canada, 2005)

- The majority of buildings are demolished before they are 30 years old.

- 35% of buildings are demolished due to area redevelopment, which can be attributed to a lack of effective planning.

- 22% of buildings are demolished due to the building being “no longer suitable for the needs”, which can be attributed to a

lack of imagination in adaptive reuse ideas.

- If these buildings were refurbished for new uses, Canada’s waste stream could be reduced by about 6%.

(Forintek Canada Corp., 2004)

### Resources

Cole, R.J. and P.C. Kernan. 1996. Life-Cycle Energy Use in Office Buildings. Building and Environment. 31(4): 307-317.

O’Connor, J. 2004. Survey on Actual Service Lives for North American Buildings. Forintek Canada Corp. Found at http://www.durable-wood.com/pdfs/Service_Life_E.pdf.

Statistics Canada. 2005. Disposal of Waste by Source, by Provinces and Territories.  Found at http://www40.statcan.ca/l01/cst01/envi25a.htm?sdi=construction %20demolition.

Trusty, W. B. 2004. Renovating vs. Building New:  The Environmental Merits. The Athena Institute. Found at http://www.athenasmi.ca/publications/docs/OECD_paper.pdf.